IP COMPONENTS

Every IP component is associated to a set of files characterized by the following directory structure:

The <component_name>_hw.tcl file describes the hardware side of the component. It can be created using the Platform Designer Component Editor and it includes the following elements:

- Information about the component, such as name, version and author
- HDL description of the component’s hardware
- Constraint files (sdc and/or qip) that define the component for synthesis and simulation
- Component’s interfaces, including I/O signals
- Parameters that configure the operation of the component

Using the Component Editor we can enter information, parameters, constraint files, signals and interfaces. Then, it is possible to automatically generate the top-level HDL file (go to the Files tab and click on Create Synthesis File from Signals), which must be edited to add the logic that describes the component's behavior, and the whole <component_name>_hw.tcl file (clicking on Finish). All the HDL files and the constraint files are inserted in the hardware/ directory.

An IP component can be associated (although it is not strictly necessary) to a custom HAL device driver able to interface it to the HAL, so that it can be easily managed in SBT while creating the software for a Nios II system. Every HAL device driver has its own software description file, named <component_name>_sw.tcl, which is created using the following Tcl commands:

The first command must be the create_driver command. It is recommended to choose the name <custom_component>_driver for the driver:
create_driver <custom_component>_driver

Identify the hardware component class the driver is associated with using the set_sw_property command’s hw_class_name argument:
set_sw_property hw_class_name <hardware_class>

Specify each BSP type supported using the add_sw_property command’s supported_bsp_type argument (in our case it must support just the Intel FPGA HAL):
add_sw_property supported_bsp_type hal

Specify each source file using the add_sw_property command’s c_source argument:
add_sw_property c_source HAL/src/driver_source_file.c

Specify each header file using the add_sw_property command’s include_source argument:
add_sw_property include_source inc/<custom_component>_regs.h
add_sw_property include_source HAL/inc/<custom_component>.h
- Enable HAL autoinitialization mechanism (if necessary):
  set_sw_property auto_initialize true

The autogenerated source file alt_sys_init.c contains the alt_sys_init() function, which is called before the main() function to initialize the device drivers. If a driver uses the HAL autoinitialization mechanism, the generated alt_sys_init.c file invokes <component_name>_INSTANCE and <component_name>_INIT macros, which must be defined in the <component_name>.h header file.

Other than the <component_name>_sw.tcl file, a solid device driver contains also a header file defining the hardware interface of the component, called <component name>_regs.h. In particular, it provides access to the interface registers by means of suitable IORD/IOWR functions.

When a custom IP component is created using the Platform Designer Component Editor, only the hardware files are present. If we include it in a Platform Designer System and we create an SBT project, we do not have a HAL device driver, therefore we do not have a <component name>_regs.h file to exploit in order to interface the component. If we do not want to create it, we can use a generic driver for a generic memory-mapped device called io.h, which is automatically included in any SBT project. In particular, it contains the following #define directives:

#define IORD(BASE, REGNUM)
#define IOWR(BASE, REGNUM, DATA)